## Slide 1
Creating closed-loop Brain-Computer Interfaces (BCIs) for Prosthetics
Studying neuron circuits and their contributions to behavior for Neurotherapy
  NHPs are ideal candidates of study for their physiological similarities to humans
  [1]
Stimulating the Brian
Closed-loop Brain Stimulation in NHPs
Using Hardware Accelerated Machine Learning
Rajeev B. Botadra¹, ChiJui Chen⁵, Leo Scholl¹, Trung Le¹, Hao Fang¹, Ryan Canfield², Amy Orsborn¹, Eli Shlizerman³, Shih-Chieh Hsu⁴, Scott Hauck¹
NSF-2117997
Electric stimuli can incite/inhibit neuron activity
Occurs over an order of milliseconds
Need a system that operates within latency constraint to effectively target brain regions
Motivations
Latency Constraint & FPGAs
Decoding Neural Activity
The pre-trained LFADS model weights were quantized with QAT
LFADS Kernel resource utilization on U55C
LFADS – a Variation Autoencoder – models firing activity in brain regions
[2]
Decoded brain states inform the stimulation pattern to inhibit neurons and observe the response
Higher firing activity during stimulation can constrain inference latencies to <20ms (1/F)
Modern CPUs and GPUs fail to meet this constraints on sequential architectures, so we look to FPGAs
The existing experimental apparatus was modified to integrate the FPGA and build an online closed-loop system
Raw field potentials are preprocessed into spikes before decoding
LFADS kernel deploys a fine-tuned and quantized architecture
System Design
Decoder Accuracy
Test and deploy additional model architectures (NDT, MRAE, modified LFADS)
Leverage closed-loop capability in experiment design
  Investigating motion pre-planning through the hand-reach-out task
Future Works
[1] Nan Qiao, et al. “Update on Nonhuman Primate Models of Brain Disease and Related Research Tools.” MDPI Biomedicines, 2023.
[2] Xiaohan Liu, et al. “Sleep Spindles as a Driver of Low Latency, Low Power ML in HLS4ML & TinyML.” University of Washington, 2023.
References
¹Electrical & Computer Engineering, University of Washington
²Bioengineering, University of Washington
³Applied Mathematics, University of Washington
⁴Physics, University of Washington
⁵Electrical Engineering, National Yang Ming Chiao Tung University